# 1999 Performance / Price Sort and PennySort

Brad Helmkamp

Keith McCready

April 21st, 1999

Research and Development

Stenograph LLC

1500 Bishop Ct.

Mt. Prospect, IL 60056

# 1999 Performance / Price Sort and PennySort

Brad Helmkamp, Keith McCready, Stenograph LLC

helmk@msn.com keithmc@ix.netcom.com

March 1999

Abstract:  HMSort is a minimal functionality external sort written to demonstrate the advantages of combining overlapped IO with a well thought out sorting algorithm.  The PennySort, a type of sorting benchmark designed to run on inexpensive machines available to the average user, is a good place to demonstrate what can be gained by using this programming approach.  HMSort was able to sort 2.58 GB for a penny, not quite double last year’s performance.  For a direct comparison, we also ran last year’s Indy winner NTSort on our lower cost system. NTSort was able to sort 1.98 GB for a penny.  This paper documents these results and also provides performance data on the Datamation and the proposed Performance/Price sort benchmarks.

Why Stenograph LLC?   Stenograph LLC is a company dedicated to providing stenographic transcriptionists with the highest quality supplies and productivity tools.  Court reporters, who make up the majority of our market, use computer based dictionaries of up to 250,000 entries to provide a mapping from their shorthand to English words and phrases.  Managing these dictionaries has traditionally been a time consuming activity with limited functionality.  With the use of efficient sorting, we are removing the frustrations of waiting on the software to complete dictionary tasks and providing functionality that was not available before.  By entering the PennySort competition we hoped to learn from and compare ourselves to the current sort programs on the market.

## 1999 Indy PennySort

Problems with selecting a system:   Purchasing a system for the competition turned out to be a frustrating experience.  Initially, we were not aware any guidelines existed for what was required, and there was no guarantee that someone wouldn’t just purchase a refurbished 486 system and have a disproportionate amount of time to run their sort. It would be a shame to turn this merely into a shopping competition – especially as we seemed to have more trouble with shopping than with debugging our program.  We placed several orders with vendors who had what we needed “in stock” only to find our order canceled later due to “lack of stock”.

There are good reasons, however, to allow individuals to choose their own hardware.  If someone can tailor their sort to use the cache on a particular processor to their advantage they should be allowed to do so.  Also, on a cost/speed basis, it could be useful to compare multiple to single processor systems, or an alternative mass storage device to traditional hard drives.

Our view is that the focus of the competition should be on understanding and using the latest hardware to its fullest potential.  That would be easier if there were a specification for what parts constitute a minimum PennySort machine.  Obviously that should include:

a)    Processor(s)

- Case, Power Supply, and Motherboard

- Memory

- Operating System

- Storage Device(s) (to hold original file, resultant file, and all temporary files)

and anything else necessary to run the sort program.  Other parts like monitor, CDROM, floppy disk, etc. could be ignored.  It would also alleviate shopping fears if all entrants were given the opportunity to run their sort on the winner’s machine choice for the final results.

Our Choice:   Because IO is the bottleneck on large sorts, we focused on getting the fastest hard drives for our money rather than more memory or a faster CPU.  We considered SCSI drives in a RAID 0 configuration, but the additional cost of 3 or 4 drives plus a SCSI controller outweighed the performance that would be gained.  Turning to IDE drives, we found that Ultra ATA/66 drives were available, but we chose Ultra ATA/33 drives instead.  Although data can move between the disk cache and main memory twice as quickly with Ultra ATA/66 drives, the internal transfer rate from the disk media into the drive’s cache depends on rotational speed and media density.  We found that the Ultra ATA/66 drives that were available had the same internal transfer rate as the Ultra ATA/33 drives, around 15MB/sec max.  As we were dealing with over 2.5 GB of data, we expected the drive’s internal cache to be flooded nearly all the time, making the transfer rate to and from the media the most important measure of the drive’s performance.

For comparison with last year’s 3.1 GB Ultra ATA/33 5400rpm drives, we used the UNBUFCPY sample program from the Win 32 SDK to move 1.41GB (15,000,000 101 byte records) from one disk to the other.  This copy finished in 118.7 seconds with 7.9 seconds of that being User or Kernel time.  A full two pass sort moves the sort data to and from disk twice.  This means that there would be a minimum of 221.6 seconds of data IO when sorting a 1.41 GB file on our machine. This is 46% less time than last year’s 411 seconds to do the same task.

Applying the same unbuffered copy to this year’s 2.58 GB of data shows that the IO portion of the two pass sort takes 431.3 seconds.  (A one way copy took 227.9 seconds elapsed time and 12.2 seconds User or Kernel time.)  This is the theoretical minimum amount of time the sort could take.

As was done last year, we shopped on the web at www.pricewatch.com for our hardware, trying to stay around $1,000.  We purchased our system from Nova Computers of Texas (www.novatexas.com) who seemed to have the lowest prices on pricewatch for many systems.

Our PennySort system is described in Table 1:

| Table 1: Price breakdown of 1999 PennySort Machine |  |  |  |
| --- | --- | --- | --- |
| Quantity | Description | Cost | Total |
| 2 | 7.5 GB UDMA 7200 rpm Maxtor DiamondMax+ Hard Drive | $214.40 | $428.80 |
| 1 | 333 Pentium II Processor W/ Bx Motherboard, Mini Tower Case, power supply, and 8M AGP Video 3D | $308.00 | $308.00 |
| 1 | 64 MB 8 ns SDRAM PC100 | $94.00 | $94.00 |
| 1 | Windows NT 4.0 Operating System | $99.00 | $99.00 |
| 1 | 3.5 inch Floppy Drive | $14.00 | $14.00 |
| 1 | ACER 10/100Mbps Network Card | $25.00 | $25.00 |
| 1 | Assembly | $15.00 | $15.00 |
| 1 | Shipping | $48.08 | $48.08 |
| Total |  |  | $1031.88 |

The time budget for the PennySort assumes a three year depreciation of the hardware and is calculated, therefore, by dividing the number of seconds in three years (94,608,000) by the system cost.  Our system cost of $1031.88 yields 917 seconds/penny.

The prices of systems are continually dropping.  In addition to our 333 MHz Pentium II system, we had hoped to report results on an $868 300 MHz non-Pentium system which would have given 1090 seconds in which to run.  Unfortunately, we were not able to make the disk subsystem run reliably.  We found that the final sorted file contained a small (32 byte) error.  We spent a couple days trying to find out what was wrong with our sort program.  We were quite puzzled until we found that, when checking whether the intermediate merge files were correctly sorted one of them failed the test.  Then, seconds later, the same file passed the test.  We then realized that we could not reliably read from our drives with this system.  To be certain, we copied a correctly sorted file from one drive to the other.  Checking it showed another error.  We tried the latest IDE drivers, but the problem persisted.  Not having the time to determine where the problem lay exactly (memory timing, bus master IDE drivers, system board,, etc.), we returned to our 333 MHz system.

Results: We tested three sorts on Windows NT 4.0 Service Pack 4:

- HMSort -- our own combination sort that is not yet commercially available

- NTSort – a version of the NT 5.0 Beta sort that runs on NT 4.0 supplied by Jim Gray

- The Postman’s Sort™ v 3.25 by Robert Ramey commercially available for $49 for a two year license

We generated files with 100-byte records using a modified version of the SortGen program.  We ran each of the sorts with several different sizes of files searching for the maximum amount they could sort in 917 seconds.  We decided not to normalize the results because sort time does not always increase in a linear fashion.  For example the normalized results would indicate that HMSort could only sort 172.8 MB in a minute, but it was actually able to sort 210.8 MB in a minute.

Unfortunately the Postman’s Sort™, which was last year’s Daytona winner, was unable to sort files near or above 2GB.  We discussed this with Robert Ramey and he confirmed this to be a problem.  He has an excellent sorting program, however, so we have included results in the Performance/Price and Datamation sections of this paper.

We made a post-April 1st version of HMSort (described below in “Achieving the theoretical minimum time”) that was able to sort 30.2 million records, more than double last year’s winning value.  For this sort it turned out to be a better choice to use 128 MB of memory and a higher system cost than to stick with the 64 MB used for the pre-April tests.  The results are recorded in table 2.

| Table 2: 1999 PennySort Times. |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Product | Time Budget | Best Time | Kernel | User | Total CPU Time | Sorted GB | Category |
| HMSort | 917 | 907.5 | 27.1 | 413.7 | 440.8 | 2.58 | Indy |
| NTSort | 917 | 902.0 | 15.3 | 539.4 | 554.7 | 1.98 | Indy |
| Post-April 1st HMSort | 840 | 814.5 | 38.0 | 507.7 | 545.7 | 2.81 | Indy |

We noticed a variance of around +/- 4% in the amount of time taken by each of the PennySorts to completely sort a given file.  We speculate that the variance was produced by differing disk latency – the time taken waiting for the disk to rotate the desired sectors under the head for writing.  Normally, a large number of random reads and writes would average out to a consistent total disk latency time.  But while sorting or copying a file the writes occur a consistent amount of time after their corresponding reads, possibly skewing the average.  The amount of time this adds is leveraged by the amount of data being moved.  For example, if every read from one drive and write to the other were 64K in size, there would be 42,267 read/write pairs just to copy the 2.58 GB file.  If every write had to wait the maximum time for the disk to rotate the correct starting sector into position (one full revolution = 8.333 ms.), 352 seconds could be used up just waiting for the disk to rotate.  Fortunately, this is not the typical case as we know we can copy the file in 227.9 seconds.  But if from one run to the next the average disk latency changed by plus or minus one tenth of a revolution (0.833 ms) that could easily add up to and explain the variance we observed.

Achieving the theoretical minimum time:   HMSort gains most of its efficiency because its computation and IO are overlapped.  At 917 seconds, however, it is still a long way from the theoretical minimum of  431 seconds to perform a two pass sort on 2.58GB.

One reason a two pass sort on a file takes longer than copying the same file twice is the large amount of seeking done during the merge phase.  During the first phase there is one input file and one output file (at a time), which is identical to the copy scenario.  During the second phase of sorting, however, there are many merge files and one output file.  For instance, if the sort produces 124 21MB merge files and it reads 64K at a time, it will seek over 41,900 times before retrieving all of the data.  If each seek takes an average of 9 milliseconds, this would slow the merge phase down by 377 seconds. In order to reduce this time, as Table 3 shows, increasing the amount read at a time is more effective than using fewer merge files.

HMSort uses two buffers per file so it can overlap reading with merging.  For the 2.58GB sort the buffers were each 128K and there were 124 merge files.  This results in 189 seconds lost to seeking.

Looking for other reasons HMSort didn’t meet the theoretical minimum, we noticed calls to the Windows API function WriteFile took a disproportionate amount of time to return even though we called them as overlapped functions.  Specifically, during the time we were sorting as much as we could in a minute, 23 out of 55 seconds were spent waiting for WriteFile to return compared to 0.5 seconds spent in the similar call to ReadFile.  This means that 40% of HMSort’s user time is spent unproductively even when other reads or writes have finished and demand attention.  As a result, disk IO completes 99.6% of the time before HMSort is ready to process it.  After April 1st, we found a way to reduce the impact of this delay in WriteFile.  At the beginning of the sort we created a second thread and immediately suspended it. Whenever the main thread was ready to write something to a file it would signal the second thread.  The second thread then called WriteFile and took the delay while the main thread was free to process other IO completions.  This post-April 1st version of HMSort was able to finish sorting 2.58GB in 868 seconds, 40 seconds faster than the original.  Even more dramatic, with an additional 64MB of memory it was able to sort 2.58GB in 745 seconds, outweighing the cost of the memory.

After accounting for the seek time and WriteFile delays there are still several minutes difference between the theoretical minimum and actual sort times.  Perhaps there are ways to use IO more efficiently than HMSort does, or there may be sorting algorithms that would fit more naturally with overlapping.  This would be a good place to do research for future PennySort programs.

## Datamation Sort Results

The Datamation sort benchmark tests a one pass sort of one million 100 byte records.  Because this is a one pass sort, reading and writing cannot be overlapped with each other.  The Datamation sort, therefore, places more emphasis on the efficiency of the sorting algorithm used and on how much of its computation can be overlapped with either reading or writing.  Normally the Datamation sort does not take into account the cost of the system (the 1999 winner finished in 1.18 seconds), but because it shows the speed of a one pass sort it is valuable for comparing how the PennySort entrants perform on smaller files.

We added 64MB to the 1999 PennySort machine in order to run a Datamation Sort in one pass with each of the sorting programs.  HMSort averaged 23 seconds.  The Postman Sort averaged 25 seconds, getting its best results when we specified a buffer size of 64K. NTSort averaged 33 seconds after being given a memory hint of 105MB as was done last year.  Our post-April 1st HMSort was able to sort 1 million records in 16 seconds.

1999 Performance/Price Sort

We agree with the assertion in last year’s PennySort document that the Performance/Price Sort is a better benchmark than the PennySort for the long term.  Timing several 15+ minute sorts was a tedious task, and it will only get worse next year.  But, for the near future, we hope that results will be reported for both benchmarks, so we can see how they perform on several gigabytes of data.

Again, we chose not to normalize the results from the PennySort because sorting times do not increase linearly.  For the Postman sort we ran the test with 128 MB of memory instead of 64 MB because it performed much better for us that way.

- Sort the largest file you can in a minute.

- Divide file size in GB by 60 to calculate GB/s.

- Compute the system price in $ per second (3-year depreciation => system price divided by 9.5e-7 ).

- Compute the GB/$ sorted by dividing item 2 by item 3.

The Performance/Price results as recorded in last year’s PennySort document are shown in Table 2 with our 1999 results added onto the end:

| Table 2: Historical Performance/Price results. |
| --- |
| year | MB/sec | GB/$ | System | Sys price (M$) | CPUs |  |
| 1985 | 0.02 | 0.05 | M6800 Bitton et al | 0.03 | 1 | Datamation |
| 1986 | 0.03 | 0.01 | Tandem Tsukerman | 0.3 | 3 | Datamation |
| 1987 | 3.85 | 0.05 | Cray YMP, Weinberger | 7.0 | 1 | Datamation |
| 1991 | 14.29 | 0.54 | IBM 3090, DFsort/Saber | 2.5 | 1 | Datamation |
| 1990 | 0.31 | 0.15 | Kitsuregawa | 0.2 | 1 | Datamation |
| 1993 | 1.20 | 0.11 | Sequent, Graefe | 1.0 | 32 | Datamation |
| 1994 | 1.72 | 0.16 | IPSC/Wisc DeWitt | 1.0 | 32 | Datamation |
| 1994 | 11.11 | 5.25 | Alpha, Nyberg | 0.2 | 1 | Datamation |
| 1995 | 28.57 | 2.70 | SGI/Ordinal, Nyberg | 1.0 | 16 | Minute/Daytona |
| 1995 | 19.61 | 37.10 | IBM, Agarwal | 0.05 | 1 | Minute/Indy |
| 1996 | 100.00 | 15.76 | NOW, Arpaci-Dusseau | 0.6 | 32 | Minute/Indy |
| 1997 | 140.17 | 8.41 | Now 95 , Arpaci-Dusseau | 2.0 | 95 | Minute/Indy |
| 1997 | 86.21 | 6.27 | SGI/Ordinal, Nyberg | 1.3 | 14 | Minute/Daytona |
| 1998 | 1.74 | 125.00 | PostmanSort | 0.0013 | 1 | Penny/Daytona |
| 1998 | 1.74 | 144.00 | NTSort | 0.0012 | 1 | Penny/Indy |
| 1999 | 2.23 | 174.99 | Postman Sort | 0.0012 | 1 | Penny/Daytona |
| 1999 | 2.46 | 220.59 | NTSort | 0.0010 | 1 | Penny/Indy |
| 1999 | 3.51 | 314.51 | HMSort | 0.0010 | 1 | Penny/Indy |
| 1999 | 3.78 | 338.17 | HMSort Post-April 1st | 0.0010 | 1 | Penny/Indy |

## Conclusion

HMSort sets Performance/Price sorting records consistently for scales from as small as the Datamation benchmark up to the PennySort benchmark. These results demonstrate the value of overlapping IO with both computation and other IO operations.  There is plenty of room for improvement, however, in coming up with better sorting algorithms, improvements in the operating system, and in faster, lower cost hardware. As Knuth has pointed out, “The problem of efficient sorting remains just as fascinating today as it ever was.”

# Endnotes

Throughout this paper KB=1024 bytes, MB=10242 bytes, and GB=10243 bytes.  Therefore 27,700,000 records of 100 bytes each = 2.58 GB

http://msdn.microsoft.com/library/devprods/vs6/vc++/vcsample/vcsmpunbufcpysamplefastcopyroutines.htm

After April 1st we also tested 3wareSort from 3ware.  For a full description of how this sort works see 3ware’s submitted paper at http://research.microsoft.com/barc/sortBenchmark

Jim Gray is a senior researcher in Microsoft Research's Scaleable Servers Research Group and manager of Microsoft's Bay Area Research Center (BARC). Internet site: http://research.microsoft.com/~Gray

Robert Ramey Software Development, Santa Barbara, CA.  Internet site: http://www.rrsd.com/

We modified SortGen.c to open its file in binary mode instead of text mode.  This prevents fwrite from translating the “\x0d\x0a” into “\x0d\x0d\x0a” so the records are exactly 100-bytes as specified in the benchmark rules.

SortGen at http://research.microsoft.com/barc/SortBenchmark

PennySort.doc at http://research.microsoft.com/barc/Sortbenchmark

Knuth, D.E., Sorting and Searching, The Art of Computer Programming 2nd ed., Addison Wesley, Reading, MA., 1998, p.390